# Battle Mini Bot
## (Project Proposal)

# Overview
We propose to design and build a mini battle bot to participate in the Expecto competition. The bot will be a compact, agile, and durable combat robot, engineered for fast-paced action and strategic maneuvering in the arena. Our goal is to create a bot that excels in both offensive and defensive capabilities, utilizing advanced design techniques and components to outsmart and outperform competitors.

DESIGN
The robot design suggests a focus on durability and maneuverability. The motor/gearbox assembly is centrally located on the weapon. The horizontally spinning weapon would still function in an inverted position as it's symmetrical. The wheeled drivetrain and chassis shape suggest that the bot is likely designed for high-speed movement and the ability to absorb impacts.

COMPONENTS
● TRANSMITTER AND RECEIVER
A Transmitter is a handheld device that allows the user to control an RC car. It sends signals wirelessly over radio frequencies to the receiver in the RC car, dictating its movements. These signals are generated through channels, each representing a specific function (like steering). A receiver is the component installed in an RC car that receives signals from the transmitter. It interprets these signals and converts them into actions by controlling various servos and electronic speed controllers (ESCs). The receiver ensures that the RC car performs the desired maneuvers based on the transmitted commands.
Flysky FS-i6X 6-channel transmitter and receiver supports advanced features such as adjustable steering which are useful for fine-tuning control for better handling and performance, especially in more demanding conditions. This setup provides flexibility for future enhancements while keeping the current control system simple and effective.

● THE MOTOR
The Brushless DC (BLDC) motors are far more efficient, faster in speed, and sustain a longer period of motion than their counterparts. Greater efficiency signifies that more power is delivered forthwith to allow higher acceleration and better performance on harsh terrains. Their high responsiveness to electronic speed controllers allows for precise control over speed, acceleration, and braking, making them suitable for use. We are using two bldc motors for steering as well as speed.

● ELECTRONIC SPEED CONTROLLER AND ARDUINO SHIELD
An Electronic Speed Controller (ESC) acts as an intermediary between the battery and the motor, translating the driver's throttle input into precise motor control. The braking system can bring the speed down sharply, thereby giving better control and security. When activated, the ESC reverses the motor's polarity, causing it to act as a generator, effectively slowing the vehicle down which is crucial for maneuvers like sharp turns, avoiding obstacles, and maintaining control.
We are using a L293D Motor Driver/Servo Shield for Arduino because is probably one of the most versatile on the market and features 2 servo and 4 motor connectors for DC or stepper motors. That makes it a great shield for any robotic project. This Arduino compatible motor Driver shield is a full-featured product that it can be used to drive 4 DC motors. The shield contains two L293D motor drivers and one 74HC595 shift register. The shift register expands 3 pins of the Arduino to 8 pins to control the direction of the motor drivers. The output enables the L293D is directly connected to the PWM outputs of the Arduino.

Materials
Chasis: Aluminium; due to strength, durability and corrosion resistance aluminium material is used. Plastic; at some places if weight and balance becomes a problem.
- Tyres: Silicon rubber; due to flexibility, grip, shock absorptio rubber materials are used. ABS + 20% glass; due to its high weight bearing capacity and strength.
- Front Wheel: A castor Ball Bearing: due to its strength and freeness to move along any direction.

Team Information
Name	Contact No.
Arjun Mohan Saxena	8707619707
Chirag Nagar	7206355907
Soham Prakash Bhandare	9284455793
Pranshu Gupta	8279048848

Budget Breakdown and Purchasing Links